# Operators
### CAVEAT
Semantics pitfall!
OR corresponds to “and/or” in spoken language, while XOR corresponds to “either or”.
XOR stands for exclusive-or.
AND	1 iff[1] all inputs are 1 / 0 otherwise
OR	1 if at least one input is 1 / 0 only If all inputs are 0
XOR	1 if inputs are not the same
NOT	1 if input is 0 / 0 if input is 1
[1] iff: “if and only if”

# Bits & Bytes
8 bits make 1 byte[2].
[2] For sake of simplicity and the platform we're using, we only consider bytes in this cheatsheet
Bits are numbered from right to left.

Bit #	7	6	5	4	3	2	1	0
Value	128	64	32	16	8	4	2	1
	MSB[3]							LSB[4]
[3] MSB: Most significant bit
[4] LSB: Least significant bit

This is analogous to how the decimal system works, the more
important digits are further left. But instead of every digit having a place value of 10n binary has a place value of 2n.

# C-Style Operators
### CAVEAT
To fiddle with bits, use only bitwise operators!
Your compiler will allow you to use logical operators, but the result will not be what you want!
	Bitwise	Logical
AND	&	&&
OR	|	||
NOT	~	!
XOR	^

# Shifting
Shift all bits to the left or right en-bloc.

Bits that are "shifted out" are lost.
Replacement bits "shifted in" are usually set to 0, with one exception: Right-shifting unsigned values repeats the MSB to preserve the sign.

### Fun Fact :)
Shifting left by n places is equivalent to multiplying by 2n.
Likewise, shifting right by n places is equivalent to dividing by 2n.

	Operator
Shift Left	<<
Shift Right	>>

Operation	Unsigned Result	Signed Result
11001011 >> 2	00110010	11110010
11001011 << 2	00101100	00101100

# Masking

If you're only interested in a subset of bits, you can "select" them
using a mask.
A mask is simply a byte with a number of bits set to 1.
You can think of such a 1-bit as a cut-out in a piece of paper.
Everything that is 1 you can see, everything else (0) you cannot.
# Useful Operations
We've collected a bunch of useful operations for your convenience in the table to the right.
Enjoy & happy hacking!
Mask with nth bit set	(1 << n) / (1 << 3)	=> 00001000
Mask with nth and mth bit set	(1 << n) | (1 << m) / (1 << 3) | (1 << 7)	=> 10001000
Mask with everything but nth bit set	~(1 << n) / ~(1 << 3)	=> 11110111
Set high-bits of mask m in v	v | m / 11001100 | 01100110	=> 11101110
Clear high-bits of mask m in v	v & ~m / 11001100 & ~01100110 11001100 & 10011001	=> 10001000 / => 10001000
Toggle the nth bit	V ^ (1 << n) / 11001100 ^ (1 << 3) / 11001100 ^ (1 << 4)	=> 11000100 / => 11011100
Directly apply operations to a variable	a = a | b a = a & b a = a ^ b / a = a << b a = a >> b	=> a |= b / => a &= b / => a ^= b / => a <<= b / => a >>= b